## Slide 1: General License Course Chapter 4
Lesson Plan Module 16 –
Basic Test Equipment
Notes: <number>

## Slide 2
Analog & Digital Meters
Volt-ohm meter (VOM) is the simplest piece of test equipment
  Measures – volts, current, resistance
  Tests – continuity, diodes, transistors
Two types of VOM – Analog and Digital
  Analog meters have a moving needle and calibrated scales on the meter face
  Analog meters are useful for finding a peak or minimum reading, such as when adjusting a tuned circuit
2015 General License Course
<number>
Notes: <number>
Have an analog and digital multimeter available to illustrate the differences.

## Slide 3
Analog & Digital Meters
  Digital meters (DDMs) offer significantly greater precision than analog meters
  Digital meters have useful features:
    auto-ranging to automatically select the proper display range
    peak hold to capture maximum values
  When measuring voltage, the meter should have a high input impedance to place the minimum load on the circuit being measured
2015 General License Course
<number>
Notes: <number>
Explain that loading the circuit will cause measurement errors.

## Slide 4
Oscilloscope
The oscilloscope (or “scope”) provides a visual display of voltage against time
  Updated rapidly enough to give a real-time picture of the signal
  Fast-changing complex waveforms can be measured
  External signals are connected to horizontal and vertical channel inputs to control the display
  Variable gain and update rates are available to display many types of signals.
2015 General License Course
<number>
Notes: <number>
Explain that older scopes use a CRT like an older TV. New scopes use LCD technology like TVs and computer monitors. Some scopes use a PC for their displays.
Explain what a “time base” is and if a scope is available, show the measuring graticule and gain/speed controls.

## Slide 5
Monitoring Oscilloscope
The transmitter’s attenuated output connects to the vertical channel of the oscilloscope to monitor the signal
  Monitoring helps adjust keying waveforms, mic gain, and speech processing
  The scope shows the effects of any adjustments that might cause distortion
  A scope provides information that numeric meters can’t measure.
2015 General License Course
<number>
Notes: <number>
Notes area

## Slide 6
Impedance & Resonance Measurement
An antenna analyzer contains a CW signal generator, frequency counter, SWR bridge, and impedance meter
  Connects to the antenna feed line to measure SWR using very small signals for measurements
  Impedance measurements show resonance
  Measures feed line velocity factor, electrical length, and characteristic impedance
  Can be affected by strong nearby signals
2015 General License Course
<number>
Notes: <number>
Have an analyzer available for demonstration.
Show SWR, impedance, and resonance measurements.

## Slide 7
Field Strength & Power Meters
Field strength meters measure the electrical field of transmitted signals
Field strength meters can be used during antenna and transmitter adjustments
Field strength meters can be used to measure antenna radiation patterns
Standing wave ratio (SWR) can be measured from forward and reflected power measurements made with a directional wattmeter
2015 General License Course
<number>
Notes: <number>
Notes area

## Slide 8
Practice Questions
2015 General License Course
Notes: <number>
Notes area

## Slide 9: What item of test equipment contains horizontal and vertical channel amplifiers?
A. An ohmmeter
B. A signal generator
C. An ammeter
D. An oscilloscope
  G4B01
2015 General License Course

## Slide 10: What item of test equipment contains horizontal and vertical channel amplifiers?
A. An ohmmeter
B. A signal generator
C. An ammeter
D. An oscilloscope
  G4B01
2015 General License Course

## Slide 11: Which of the following is an advantage of an oscilloscope versus a digital voltmeter?
A. An oscilloscope uses less power
B. Complex impedances can be easily measured
C. Input impedance is much lower
D. Complex waveforms can be measured
  G4B02
2015 General License Course

## Slide 12: Which of the following is an advantage of an oscilloscope versus a digital voltmeter?
A. An oscilloscope uses less power
B. Complex impedances can be easily measured
C. Input impedance is much lower
D. Complex waveforms can be measured
  G4B02
2015 General License Course

## Slide 13: Which of the following is the best instrument to use when checking the keying waveform of a CW transmitter?
A. An oscilloscope
B. A field strength meter
C. A sidetone monitor
D. A wavemeter
  G4B03
2015 General License Course

## Slide 14: Which of the following is the best instrument to use when checking the keying waveform of a CW transmitter?
A. An oscilloscope
B. A field strength meter
C. A sidetone monitor
D. A wavemeter
  G4B03
2015 General License Course

## Slide 15: What signal source is connected to the vertical input of an oscilloscope when checking the RF envelope pattern of a transmitted signal?
A. The local oscillator of the transmitter
B. An external RF oscillator
C. The transmitter balanced mixer output
D. The attenuated RF output of the transmitter
  G4B04
2015 General License Course

## Slide 16: What signal source is connected to the vertical input of an oscilloscope when checking the RF envelope pattern of a transmitted signal?
A. The local oscillator of the transmitter
B. An external RF oscillator
C. The transmitter balanced mixer output
D. The attenuated RF output of the transmitter
  G4B04
2015 General License Course

## Slide 17: Why is high input impedance desirable for a voltmeter?
A. It improves the frequency response
B. It decreases battery consumption in the meter
C. It improves the resolution of the readings
D. It decreases the loading on circuits being measured
  G4B05
2015 General License Course

## Slide 18: Why is high input impedance desirable for a voltmeter?
A. It improves the frequency response
B. It decreases battery consumption in the meter
C. It improves the resolution of the readings
D. It decreases the loading on circuits being measured
  G4B05
2015 General License Course

## Slide 19: What is an advantage of a digital voltmeter as compared to an analog voltmeter?
A. Better for measuring computer circuits
B. Better for RF measurements
C. Better precision for most uses
D. Faster response
  G4B06
2015 General License Course

## Slide 20: What is an advantage of a digital voltmeter as compared to an analog voltmeter?
A. Better for measuring computer circuits
B. Better for RF measurements
C. Better precision for most uses
D. Faster response
  G4B06
2015 General License Course

## Slide 21: Which of the following instruments may be used to monitor relative RF output when making antenna and transmitter adjustments?
A. A field strength meter
B. An antenna noise bridge
C. A multimeter
D. A Q meter
  G4B08
2015 General License Course

## Slide 22: Which of the following instruments may be used to monitor relative RF output when making antenna and transmitter adjustments?
A. A field strength meter
B. An antenna noise bridge
C. A multimeter
D. A Q meter
  G4B08
2015 General License Course

## Slide 23: Which of the following can be determined with a field strength meter?
A. The radiation resistance of an antenna
B. The radiation pattern of an antenna
C. The presence and amount of phase distortion of a transmitter
D. The presence and amount of amplitude distortion of a transmitter
  G4B09
2015 General License Course

## Slide 24: Which of the following can be determined with a field strength meter?
A. The radiation resistance of an antenna
B. The radiation pattern of an antenna
C. The presence and amount of phase distortion of a transmitter
D. The presence and amount of amplitude distortion of a transmitter
  G4B09
2015 General License Course

## Slide 25: Which of the following can be determined with a directional wattmeter?
A. Standing wave ratio
B. Antenna front-to-back ratio
C. RF interference
D. Radio wave propagation
  G4B10
2015 General License Course

## Slide 26: Which of the following can be determined with a directional wattmeter?
A. Standing wave ratio
B. Antenna front-to-back ratio
C. RF interference
D. Radio wave propagation
  G4B10
2015 General License Course

## Slide 27: Which of the following must be connected to an antenna analyzer when it is being used for SWR measurements?
A. Receiver
B. Transmitter
C. Antenna and feed line
D. All of these choices are correct
  G4B11
2015 General License Course

## Slide 28: Which of the following must be connected to an antenna analyzer when it is being used for SWR measurements?
A. Receiver
B. Transmitter
C. Antenna and feed line
D. All of these choices are correct
  G4B11
2015 General License Course

## Slide 29: What problem can occur when making measurements on an antenna system with an antenna analyzer?
A. Permanent damage to the analyzer may occur if it is operated into a high SWR
B. Strong signals from nearby transmitters can affect the accuracy of measurements
C. The analyzer can be damaged if measurements outside the ham bands are attempted
D. Connecting the analyzer to an antenna can cause it to absorb harmonics
  G4B12
2015 General License Course

## Slide 30: What problem can occur when making measurements on an antenna system with an antenna analyzer?
A. Permanent damage to the analyzer may occur if it is operated into a high SWR
B. Strong signals from nearby transmitters can affect the accuracy of measurements
C. The analyzer can be damaged if measurements outside the ham bands are attempted
D. Connecting the analyzer to an antenna can cause it to absorb harmonics
  G4B12
2015 General License Course

## Slide 31: What is a use for an antenna analyzer other than measuring the SWR of an antenna system?
A. Measuring the front to back ratio of an antenna
B. Measuring the turns ratio of a power transformer
C. Determining the impedance of an unknown or unmarked coaxial cable
D. Determining the gain of a directional antenna
  G4B13
2015 General License Course

## Slide 32: What is a use for an antenna analyzer other than measuring the SWR of an antenna system?
A. Measuring the front to back ratio of an antenna
B. Measuring the turns ratio of a power transformer
C. Determining the impedance of an unknown or unmarked coaxial cable
D. Determining the gain of a directional antenna
  G4B13
2015 General License Course

## Slide 33: What is an instance in which the use of an instrument with analog readout may be preferred over an instrument with a digital readout?
A. When testing logic circuits
B. When high precision is desired
C. When measuring the frequency of an oscillator
D. When adjusting tuned circuits
  G4B14
2015 General License Course

## Slide 34: What is an instance in which the use of an instrument with analog readout may be preferred over an instrument with a digital readout?
A. When testing logic circuits
B. When high precision is desired
C. When measuring the frequency of an oscillator
D. When adjusting tuned circuits
  G4B14
2015 General License Course